## Slide 1: Health Care Waste Management
Khyber-Pakhtunkhwa Human Capital Investment Project (KP-HCIP)
Health Department Khyber Pakhtunkhwa

## Slide 2: Outline
Health care waste & different types of health care waste
WHO Classification of Health Care Waste & Color coding for segregation
Sources/ Sites of Health Care Waste
International, National & Local Agreements, Laws & Policies on HCW

## Slide 3: Overview
Health Care Waste Management (HCWM) is a critical component of public health and environmental protection.
It encompasses all the activities and processes involved in managing waste generated by health care facilities, including hospitals, clinics, laboratories, and other medical institutions.

## Slide 4
What is healthcare waste?
  Total waste stream from major healthcare establishments and from minor scattered healthcare activities
Notes: Instructor:
Ask participants to define healthcare wastes and identify some sources.
Discuss mismanagement of wastes:
lack of segregation
Re-use of syringes

## Slide 5: Importance of Healthcare Waste Management (HCWM)
Infection Control: Health care waste, particularly infectious waste, can be a source of infection if not properly handled and disposed of. This can lead to outbreaks of diseases within the community and among health care workers.
Environmental Protection: Improper disposal of health care waste can lead to environmental contamination, affecting soil, water, and air quality. Hazardous chemicals and pharmaceuticals can cause significant harm to ecosystems.
Occupational Safety: Health care workers are at risk of exposure to hazardous waste. Proper HCWM practices help in preventing injuries and illnesses caused by needle sticks, chemical exposures, and other hazards.
Legal and Regulatory Compliance: Compliance with local, national, and international regulations on waste management is mandatory. Effective HCWM ensures adherence to these laws, avoiding legal penalties and promoting best practices.

## Slide 6: Types of Healthcare Waste/Classification
Healthcare waste can be
  Non-hazardous general wastes comparable to domestic waste
  (75-90% of healthcare waste in a health facility)
  Potentially hazardous waste or waste that is associated with some health risks
  (10-25% of healthcare waste in a health facility)
Notes: Healthcare waste can be:
Non-hazardous general wastes, comparable to domestic wastes
Potentially hazardous waste – waste that may have associated health risks

## Slide 7: Categories of Healthcare Waste
Sharps waste
Infectious waste
Pathological waste
Pharmaceutical or cytotoxic waste
Chemical waste
Radioactive waste
Non-hazardous/general waste
Notes: See Chapter 2 of the WHO Blue Book. These categories will be discussed in greater detail in a later module.

## Slide 8: Classification of Healthcare Waste

## Slide 9
  National regulations
  International guidelines, if national regulations do not exist
Types of risk associated with waste
    Infectious disease transmission
      Waste contaminated with blood and body fluids
    Physical injury
      All sharps waste
    Chemical exposure
      Cleaning solvents
Classifications are based on:
Notes: Refer to Module 1 on classification based on health risks

## Slide 10
    Steam disinfection – infectious waste, blood or body fluids, microbiological waste
    Burial – anatomical waste, human tissues
    Incineration with pollution control – cytotoxic waste
  Waste minimization options
    Recycling – paper, glass, aluminum
    Composting – kitchen waste, ward waste
    Materials recovery – silver from x-ray waste
  Classifications are useful for deciding Treatment approaches

## Slide 11: a) Hazardous Waste:
Infectious Waste: Healthcare wastes that are suspected to contain pathogens (or their toxins) in sufficient concentration to cause diseases to a potential host after exposure.

## Slide 12: Subcategories of Infectious Wastes
Waste contaminated with blood or other body fluids
Cultures and stocks of infectious agents from laboratory work
Wastes from infected patients in isolation wards
(Sharps and pathological waste are given their own classifications because of special methods needed to handle and treat them)

## Slide 13: Waste Contaminated with Blood/Body Fluids
Examples:
  Liquid waste blood
  Cotton, gauze, or dressings saturated with blood or body fluids
  Gloves, gowns, or face masks covered in blood
Body fluids considered infectious
  Blood, blood products (e.g., plasma, red blood cells), semen, vaginal secretions, cerebrospinal fluid, synovial fluid, pleural fluid, peritoneal fluid, pericardial fluid, amniotic fluid, and body fluids that cannot be differentiated from the above-mentioned fluids

## Slide 14: Cultures and Stocks
Examples:
  Laboratory cultures used for growing microbiological agents
  Culture dishes and devices used to transfer, inoculate and mix cultures
  Stocks of infectious agents
  Discarded live and attenuated vaccines

## Slide 15: ii. Sharps Wastes
    Needles, hypodermic needles, syringes
    Scalpels and other blades
    Knives
    Infusion sets
    Saws
    Broken glass, pipettes

## Slide 16: iii. Chemical Wastes
    Toxic
    Corrosive (e.g. acids of pH < 2 and bases of pH > 12)
    Flammable
    Reactive (explosive, water-reactive, shock-sensitive)
    Oxidizing
  Non-hazardous chemical wastes do not have any of the above properties

## Slide 17: iv. Radioactive Wastes
Solid, liquid, and gaseous materials contaminated with radionuclides
Includes sealed radioactive sources, low-level waste (swabs, vials, etc.), residues, excreta from patients treated or tested with unsealed radionuclides, low-level radioactive wastewater from washing
Body fluids of patients undergoing radiation therapy

## Slide 18: b) Non-hazardous General Waste
Waste that has not been in contact with infectious agents, hazardous chemicals, or radioactive substances, and that does not pose a sharps hazard
Typically, more than half of non-hazardous general waste is paper, cardboard, and plastics

## Slide 19: Waste Color Coding: WHO Recommendation

## Slide 20: Why Segregate Healthcare Waste?
To reduce the amount of waste that must be treated as hazardous waste
To reduce the risks of exposure to hazardous healthcare waste for workers
To lower the cost of treatment and disposal of healthcare waste
To make possible the recycling of non-hazardous general waste.
General Principles
When properly segregated, 85% or more of healthcare waste is general waste with the same risk as domestic solid waste.
Sharps waste poses the highest risk of disease transmission of all waste categories
Blood and body fluids are also a significant source of disease transmission.

## Slide 21: THANK YOU